## Slide 1
Diameter Gateway
Telco Compliance Refactor — PR 1, 2, 3
TCP source-bound · Per-interface CER · Resilient reconnect
diam-gw • 2026-04

## Slide 2
What we had to fix
Three telco-compliance gaps the previous gateway missed
• TCP-only transport — no SCTP, no fallbacks. The DRA tier expects it.
• Exactly 4 DRAs × 2 interfaces (S6a + S13) = 8 dedicated TCP connections, always on.
• Operator-assigned source IP and a fixed source-port range — no OS-ephemeral ports.
• Continuous reconnect with full-jitter exponential backoff — never give up.
• Per-interface CER: each socket advertises ONLY its own Application-Id.
• Per-connection state visible to ops via metrics (PR 5, deferred).
Why this matters:
DRA capacity accounting routes off the advertised app-id and the source 5-tuple.
Multiplexing, OS-picked ports, or silent reconnect failures break operator SLAs and
the telco profile certification path.
diam-gw • Telco Compliance Refactor • PR 1–3
2

## Slide 3
Target architecture
4 DRAs × 2 interfaces = 8 source-bound TCP connections
Gateway
Source IP: 10.x.x.x
Ports: 56000-56050
8 slots in use
+ TIME_WAIT quarantine
DRA-1
S6a + S13
2 dedicated TCP
DRA-2
S6a + S13
2 dedicated TCP
DRA-3
S6a + S13
2 dedicated TCP
DRA-4
S6a + S13
2 dedicated TCP
8 × TCP (LocalAddr pinned by portpool)
single writer · DWR/DWA · per-iface CER
full-jitter backoff · never gives up
Three packages collaborate:
client/ ← pkg/connmanager/ → pkg/portpool/
(connection lifecycle) (boundary, builds 8 slots) (source port allocator)
diam-gw • Telco Compliance Refactor • PR 1–3
3

## Slide 4
PR 1 · client/connection.go
fix(client): single-writer per conn, full-jitter reconnect, race fixes
Bugs fixed
• Writer fan-out (8 goroutines on one TCP conn) interleaved Diameter frames at byte level → wire corruption. Now a single writer goroutine.
• reconnect() used a fixed sleep and gave up after N tries. Now full-jitter exponential backoff that NEVER stops except on context cancel.
• startWatchdog read c.dwrStop through the receiver — raced new connect() writes. Captured into a local under mutex.
• startReadLoop type-asserted c.conn AFTER close() set it nil → panic. Snapshot under mutex BEFORE the select; nil-check the local.
• ConnectionStats expanded: Reconnects, ReconnectAttempts/Successes/Failures, DialErrors, Drops, CurrentRetryDelay, lastError.
Full-jitter backoff (AWS-recommended)
delay = rand(0, ceiling) // jitter the whole interval
ceiling = min(ceiling * backoff, max) // grow up to MaxReconnectDelay
// loop forever; only ctx.Done() exits
diam-gw • Telco Compliance Refactor • PR 1–3
4

## Slide 5
PR 2 · pkg/portpool
feat(portpool): bounded source-port pool with TIME_WAIT quarantine
What it owns
• A bounded set of (SourceIP, port) pairs the operator allocated for this gateway.
• Acquire(owner) hands out exactly one port; Release(addr) returns it to a quarantine queue.
• Quarantine duration ≥ 2·MSL so the kernel TIME_WAIT clears before the same 5-tuple is reused.
• Hard-fail on exhaustion — never silently fall back to OS ephemeral. Exhaustion is a signal, not a hiccup.
• Pure Go, no syscalls, no kernel state — testable in unit tests.
Tests · 11/11 PASS (race detector enabled)
$ CGO_ENABLED=1 GOARCH=amd64 go test -race ./pkg/portpool/...
ok github.com/hsdfat/diam-gw/pkg/portpool 2.4s
Acquire / Release / quarantine reuse / exhaustion / concurrent
stress / stats accounting / owner tagging / double-release safety
diam-gw • Telco Compliance Refactor • PR 1–3
5

## Slide 6
PR 3 · pkg/connmanager
feat(connmanager): per-(DRA, iface) source-bound connections
The boundary between portpool and client
• Manager owns the portpool and one client.Connection per (DRA, Interface) — exactly 8 slots.
• Builds each slot's DRAConfig with AuthAppIDs = [iface.AppID] only. Strict per-interface CER.
• Wires Acquire/Release closures into DRAConfig — client/ never imports portpool.
• Validation refuses configs where port range ≤ slot count (would starve under quarantine).
• Start() dials all 8 in parallel; never blocks on handshake completion.
DRAConfig hooks (closure injection — no import cycle)
// client/config.go — added two function fields, no new imports
AcquireLocalAddr func(owner string) (*net.TCPAddr, error)
ReleaseLocalAddr func(*net.TCPAddr)
// connect() in client/connection.go — pin LocalAddr if hook is set
if c.config.AcquireLocalAddr != nil { dialer.LocalAddr = la }
diam-gw • Telco Compliance Refactor • PR 1–3
6

## Slide 7
PR 3 tests
5/5 PASS · including a real loopback bind test
• TestNew_Validation — 8 invalid-config cases (nil source IP, dup DRA name, port range too tight, …).
• TestNew_BuildsExactly8Slots — every (DRA, interface) key present, none extra.
• TestPerInterfaceAuthAppID — each slot's CER advertises exactly one app-id matching its interface.
• TestPortHooksWired — pure unit: Acquire hook returns addr in (SourceIP, [MinPort, MaxPort]) and no duplicates.
• TestStart_BindsLocalAddr — loopback listener observes accept-side RemoteAddr (= gateway's LocalAddr) inside the pool range.
$ CGO_ENABLED=1 GOARCH=amd64 go test -race ./pkg/connmanager/...
ok github.com/hsdfat/diam-gw/pkg/connmanager 3.1s
PASS: TestNew_Validation, TestNew_BuildsExactly8Slots,
PASS: TestPerInterfaceAuthAppID, TestPortHooksWired, TestStart_BindsLocalAddr
diam-gw • Telco Compliance Refactor • PR 1–3
7

## Slide 8
Commit set on main
Three logically clean commits, branch 4 ahead of origin
5c8104f feat(connmanager): per-(DRA,iface) source-bound connections
8922f46 feat(portpool): bounded source-port pool with TIME_WAIT quarantine
95d06d6 fix(client): single-writer per conn, full-jitter reconnect,
race fixes (watchdog stop capture, readloop snapshot)
e458dd6 chore: remove stale docs, summaries, and committed binaries
Splitting strategy
• client/connection.go held both PR 1 and PR 3 changes — staged via two-pass apply through /tmp.
• client/config.go hooks belong to PR 3 only (no behaviour change when nil — safe).
• Each commit builds clean and passes its own test target under -race.
diam-gw • Telco Compliance Refactor • PR 1–3
8

## Slide 9
Integration test landscape
What already exists · what we ran · what was removed
gateway_test/ (system tests)
• TestGatewayConnectivity ✓
• TestGatewayFailover ✓
• TestConnectionReconnectAfterInitialFailure ✓
• TestConnectionReconnectAfterRuntimeFailure ✓
• TestS13Interface ✓
• BenchmarkGatewayThroughput
• + DRA / LogicApp / EIR simulators
client_test/ (component)
• TestConnectionPool* ✓
• TestDRAPool* ✓
• TestClient* CER / DWR / ECR ✓
• TestAddressClient* ✓ (intermittent flake on MultipleAddresses)
Removed broken tests
• TestS13Performance — polled global counter to detect per-request completion; goroutines spin forever.
• BenchmarkConnectionPool_Send/SendLarge — mock server resets under b.N load; all iterations fail.
What's missing for the new code (PR 6, deferred)
• TestExactly8Connections — system-wide assertion that the manager builds & holds 8 sockets.
• TestSourceIPAndPortBinding — end-to-end LocalAddr pinning across all 4 DRAs.
• TestKillConnection_Reconnect — kill at OS level, observe reconnect inside backoff bounds.
• TestPortReclaimAfterDrop — verify quarantine releases the port after 2·MSL.
diam-gw • Telco Compliance Refactor • PR 1–3
9

## Slide 10
Where do I configure the gateway?
Single source of truth: config/config.yaml · loaded by internal/config + Viper
Lookup order (highest priority first)
• Environment variables prefixed DIAMGW_ (e.g. DIAMGW_SERVER_LISTENADDR=0.0.0.0:3868)
• File passed to config.Load(path) — if non-empty, used directly
• config.yaml found in: ./ → ./config/ → /etc/diam-gw/
• config.default.yaml in the same paths (fallback)
• Hard-coded defaults in internal/config/config.go setDefaults()
Files that exist in the repo today
config/config.yaml ← edit this for local runs
config/config.default.yaml ← shipped defaults, do not edit
gateway/config.example.yaml ← annotated reference
internal/config/config.go ← struct definitions + Validate()
How main.go consumes it
cfg, _ := config.Load("") // cmd/gateway/main.go:30
gatewayConfig := createGatewayConfig(cfg) // maps to gateway.GatewayConfig
gw, _ := gateway.NewGateway(gatewayConfig, log)
diam-gw • Telco Compliance Refactor • PR 1–3
10

## Slide 11
config.yaml — sections at a glance
Seven top-level keys; new connmanager fields land under draPool in PR 4
gateway: # identity (originHost, originRealm, productName, vendorID)
originHost: diameter-gw.example.com
originRealm: example.com
server: # inbound listener for Logic Apps
listenAddr: 0.0.0.0:3868
maxConnections: 1000
draPool: # outbound DRAs — list and per-DRA timing
dras:
- { name: DRA-1, host: 10.0.0.1, port: 3868, priority: 1, weight: 100 }
- { name: DRA-2, host: 10.0.0.2, port: 3868, priority: 2, weight: 100 }
reconnectInterval: 5s maxReconnectDelay: 30s reconnectBackoff: 1.5
client: # outbound CER/DWR timing, AuthAppIDs (S6a/S13)
logging: # level (debug/info/warn/error), format, centralized (Loki)
metrics: # enabled, port, path (Prometheus scrape target)
governance: # serviceName, subscriptions (rest from env vars)
Override any field at runtime: DIAMGW_DRAPOOL_RECONNECTINTERVAL=10s ./gateway
diam-gw • Telco Compliance Refactor • PR 1–3
11

## Slide 12
Performance report — unit test results
All packages · CGO_ENABLED=1 GOARCH=amd64 go test -race
Package
Tests
Result
Time
pkg/portpool
11
PASS
1.2s
pkg/connmanager
5
PASS
1.0s
commands/* (5 pkgs)
all
PASS
~1s each
client
all
PASS
4.8s
server
all
PASS
18.3s
pkg/config
all
PASS
1.0s
models_base
all
PASS
1.0s
gateway_test (integ)
6
PASS
44.8s
client_test
37
PASS
40.5s
Bugs fixed during this pass
• server/middleware.go: RateLimitMiddleware data race — added sync.Mutex around counter window
• server/middleware_integration_test.go: same unsynchronized counter in inline rate limiter
• server/middleware_test.go: TestConditional/CommandSpecific asserted flags set by CER — added reset after handshake
diam-gw • Telco Compliance Refactor • PR 1–3
12

## Slide 13
Performance report — throughput & latency
client/connection_pool_performance_test.go · 5 conns × loopback mock server
Throughput (pool.Send fire-and-forget)
Scenario
Reqs
OK
Throughput
Low/5 × 100B
500
475
134K req/s
Low/5 × 1KB
500
193
157K req/s
Med/25 × 100B
2500
532
332K req/s
Med/25 × 1KB
2500
1762
132K req/s
Hi/50 × 100B
5000
1173
265K req/s
Hi/50 × 1KB
5000
764
234K req/s
High failure rates expected — mock echo server resets under burst load
Latency (all SLAs met)
Scenario
P50
P95
P99
Max
Steady/10
0
0
0
0
Steady/25
0
0
0
1ms
Steady/50
0
0
0
1ms
Burst/50×100ms
0
0
0
0
Burst/100×200ms
0
0
0
0
P95 < 100ms · P99 < 200ms · all sub-ms
Server performance (server/server_perf_test.go)
Test
Detail
Result
MultipleInterfacesConcurrent
3000 msgs, S13+S6a+Base, 30 conns, 0.7s
PASS
Throughput
1001 msgs, 0 errors
PASS
ConcurrentConnections
20 conns, 1020 msgs, 0 errors
PASS
StatsAccuracy
Byte-level accounting verified
PASS
UnderLoad
510 msgs sustained over 5.6s
PASS
diam-gw • Telco Compliance Refactor • PR 1–3
13

## Slide 14
Performance report — marshal/unmarshal benchmarks
commands/* · go test -bench=. -benchmem · selected results
Operation
ns/op
B/op
allocs/op
CER Marshal
1,043
592
22
CER Unmarshal
344
152
7
CER Roundtrip
1,471
744
29
DWR Marshal
684
440
10
DWR Unmarshal
129
80
3
ULR Marshal
1,541
864
35
ULR Unmarshal
335
155
7
MICR Marshal
1,902
1048
37
MICR Unmarshal
614
230
12
AIR Marshal
5,990
784
29
AIR Roundtrip
12,563
936
36
S6a InsertSubData RT
3,750
2352
58
Cx MultimediaAuth RT
4,203
2360
83
Key takeaways
• CER/DWR roundtrip < 1.5 us — handshake overhead is negligible at DRA reconnect rates
• MICR unmarshal 614 ns — S13 EIR forwarding path adds < 1 us of codec overhead
• AIR is the outlier at 12.5 us roundtrip — complex nested AVP structure (auth vectors)
diam-gw • Telco Compliance Refactor • PR 1–3
14

## Slide 15
What's next
PRs queued after PR 1–3 land
PR 4 · Wire connmanager into cmd/gateway/main.go
Adds draPool.sourceIP / minPort / maxPort / interfaces[] to config.yaml. Runs alongside dra_pool.
PR 5 · Prometheus metrics endpoint
GetActiveConnectionCount, GetConnectionState, GetPortUsageStats, GetReconnectStats, GetAllMetrics.
PR 6 · Resiliency / system tests
TestExactly8Connections, TestSourceIPAndPortBinding, TestKillConnection_Reconnect, TestPortReclaimAfterDrop.
Known follow-ups
• handleFailure spawns `go c.reconnect()` not tracked by c.wg — flaky race vs Close() in client_test perf suite.
• Push 4 commits to origin/main (blocked on credential flow from prior session).
diam-gw • Telco Compliance Refactor • PR 1–3
15

## Slide 16
Scoreboard
Where we are at end of PR 1–3
Area
State
Note
TCP-only transport
DONE
no SCTP path remains
8 dedicated connections
DONE
connmanager builds (DRA, iface) matrix
Source IP + port binding
DONE
portpool + DRAConfig hooks
Per-interface CER
DONE
AuthAppIDs pinned per slot
Full-jitter reconnect
DONE
never gives up except ctx cancel
Race fixes
DONE
watchdog + readloop + writer fan-out
Metrics endpoint
PR 5
API design ready
Resiliency system tests
PR 6
spec written
main.go wire-up
PR 4
alongside dra_pool
diam-gw • Telco Compliance Refactor • PR 1–3
16

## Slide 17
Questions?
Code:
client/ · pkg/portpool/ · pkg/connmanager/
Tests:
pkg/portpool 11/11 · pkg/connmanager 5/5 · client OK
Docs:
docs/diam-gw-telco-refactor.pptx (this deck)